## Slide 1: Basic School Networking
Connecting teachers and students to access the tools and resources they need

## Slide 2: Purpose of this document
Introduce basic networking concepts to novice technicians in positions to support school networks
Define basic vocabulary as it relates to equipment, concepts and configuration
Point out pitfalls, misconceptions, and other “gotchas” that cause poor security, viruses, lost documents, and corrupt systems
Describe recovery methods for documents, user accounts and whole computer systems
As each page of this guide is dedicated to one device or service, separate detailed guides for each will be made available in the future

## Slide 3: Essential Network Components: Modem
Connects school network to wider Internet via ISP (Internet Service Provider)
Meaning: MODulator/DEModulator – This is the device that converts network packets to analog signal (MODulates) and incoming analog signal to network packets (DEModulates)
Often, this is a Cable or DSL modem, so will have a telephone or coaxial cable (like that connected to your TV) and in the near future may be fiber-optical,
Usually this is connected to a router/gateway/firewall device, but often the ISP devices contain this functionality, so may be connected directly to your network switches.

## Slide 4: Essential Network Devices: Interjection
The devices next in line include a router, firewall, gateway and switch, though often these are contained in one device, even integrated with the modem.
Though a school network may contain hundreds or even thousands of devices, the multiple ports in a switch on an integrated device may help to separate parts of your network or simply to connect multiple backbone devices, such as high-bandwidth switches
A separate device for routing will often contain a software firewall (the router often referred to as a “hardware firewall” though actually the software is what helps secure the internal network from outside threats) and be a gateway between your network and the Internet

## Slide 5: Essential Network Devices: Router/Firewall/Gateway
This device connects the school network to the Internet
Looks like one computer to the rest of the world
Firewall protects all computers on the internal network
NAT (Network Address Translation) allows all internal devices to communicate with computers (servers) on the Internet

## Slide 6: Essential Network Devices: Switches
These contain several ports (usually 8 or more, often more than 24)
Each port is usually equal on the network, though some may allow for higher-bandwidth links between switches (such as 10Gb fiber between multiple gigabit switches)
Every device connected to a switch may communicate with any other device, unless some configuration disallows it. If you are buying new devices or inheriting a prebuilt network, assume there is no such configuration unless you notice a complete lack of communication between specific devices, such as student computers unable to print to a networked printer designated for teacher use

## Slide 7: Essential Network Devices: Server
A computer with high-end specifications designated to run essential network services
To ensure stability and reliability, often multiple servers are configured to run services redundantly
Some of these services are often integrated with the router device, though in large networks these are turned off in lieu of or made redundant by dedicated server computers
These services will be provided by software running on top of a normal operating system, such as Windows, Mac OS, or Linux, even a free BSD derivative OS

## Slide 8: Essential Network Services: Dynamic Host Command Protocol
If you were to configure static IP information for each device on a network to connect manually, you would spend your whole day typing in IP address, subnet, router and DNS configuration by hand, to each computer, for about a month. When your network grows, you would have to change these settings again by hand
DHCP allows you to configure the common network settings for a group of devices, or even for your whole network, especially since subnet, router and DNS will be the same for all devices in a group, if not your entire network, and IP will differ only slightly per device.

## Slide 9: Essential Network Services: Domain Name Service
Each device on a network has a unique IP address, but referring to each by IP would be exhausting, like remembering the phone number for every person in your neighborhood PLUS anyone you frequently talk to in town AND out-of-town, out-of-state or international friends and relatives
DNS allows you to associate a name, including or without domain – such as HS-Server01.district.edu, OfficeCopier or TeacherLaptop01– and will look up the IP for you, return it to your computer (which you’re using to connect to the remote device) which will then “call” that device directly by IP